## Slide 2: Steps in Quartus FPGA Design
Creating Quartus Project
Creating Design Files (+edit)
Compiling Designs
Pin Assignments
Programming to Board

## Slide 3: Creating Project (1)
Open Quartus 18.1

## Slide 4: Creating Project (2)
File >> New Project Wizard...
next

## Slide 5: Creating Project (3)
Directory, Name, Top-Level…
Directory : C/altera/project1
Project-Name : project1
Top-level : project1
Note : Create the new directory if necessary

## Slide 6: Creating Project (4)
Project Type : Empty Project
next

## Slide 7: Creating Project (5)
Add files :
next

## Slide 8: Creating Project (6)
Family, Device, Board Setting
Name Filter :
5CSXFC6D6F31C6
Next

## Slide 9: Creating Project (7)
EDA Tool Setting
Next

## Slide 10: Creating Project (8)
Summary :
Make sure like this example
Finish

## Slide 11: After Creating Project Step

## Slide 12: Creating Design Files: Verilog
File  New
Verilog HDL File
OK

## Slide 13: Creating Design Files: Verilog
In the Editor windows, add :
module project1 (
input wire a,
input wire b,
output wire y
);
assign y = a & b;
endmodule

## Slide 14
File  Save As
project1.v
Then :
Project  Add Current File to Project

## Slide 15: Analysis & Synthesis
Set Top Level :
Change Hierarchy to Files
In project1.v > right-click > Set as Top Level ….
Analysis & Synthesis :
below “Compile Design”
Right-Click at “Analysis & Synthesis”  Start

## Slide 16: Pin Assignment
Assignments  Pin Planner
There are your input-output port
Fill in the “location”
a  pin_AB30
b  pin_Y27
y  pin_AA24
Press enter after each line
File  close (close the Pin Planner)

## Slide 17: Compile Design
Processing  Start Compilation
Or
Right-Click in “Compile Design” > Start

## Slide 18: Programming the FPGA
Connect your Board to PC and power
Power up the board
Tools  Programmer
Auto Detect  choose “5CSXFC6D6”
OK
YES

## Slide 19
In File for 5csx… device  double click
Choose Output_files folder
Choose project1.sof
Open

## Slide 20
Check Program/Configure
Click Start
If success, progress bar will be green

## Slide 21: Try the Board
Change the SW0 & SW1
See what happen in the LED-RED-0

## Slide 22: Blinking LED

## Slide 23: New Project : Blinking 1 LED
Same project setting as before
Different Verilog
Different pin assignment  additional CLK pin
Test
Create your own creation

## Slide 24: Verilog of Blinking
module blink (
input wire clk, // 50 MHz clock
output reg led = 0;
);
localparam integer HALF_PERIOD = 25_000_000; // 50,000,000 Hz / 2 = 25,000,000 cycles per half-period
reg [24:0] counter = 0; // 25 bits: max count needed is 24,999,999 (fits in 25 bits)
always @(posedge clk) begin
if (counter == HALF_PERIOD - 1) begin
counter <= 25'd0;
led <= ~led;
end else begin
counter <= counter + 1'b1;
end
end
endmodule

## Slide 25: Pin Planner
Find clk and led port
Set the location to :
Clk  pin_AF14
Led  pin_AB23

## Slide 26: Program the FPGA
Do just like previous project
See what happen to the board

## Slide 27: Multi-LED blink

## Slide 28: Multi-LED blink Verilog
module project1 (
input wire clk, // 50 MHz clock
input wire rst_n, // active-low reset
output wire [3:0] led
);
localparam integer HALF_PERIOD = 25_000_000; // 50,000,000 Hz / 2 = 25,000,000 cycles per half-period
reg [24:0] counter = 0; // 25 bits: max count needed is 24,999,999 (fits in 25 bits)
reg [3:0] count_out = 0;
always @(posedge clk or negedge rst_n) begin
if (!rst_n) begin
counter <= 25'd0;
count_out <= 4'd0;
end else if (counter == HALF_PERIOD - 1) begin
counter <= 25'd0;
count_out <= count_out + 1'b1;
end else begin
counter <= counter + 1'b1;
end
end
assign led = count_out;
endmodule

## Slide 29: Board’s Pin Assignment
DE10-Standard Manual  https://github.com/rizki-ap/VLSI/
Now we have new reset button

## Slide 30: Another Project
Input : 4 switch Button
Output : 7-segment led
Use AI to help