## Slide 1: SoC Project

## Slide 2: Creating Quartus Project
Project Directory : C:/Altera/project_soc
Project name :
project_soc

## Slide 3: Add Verilog files
module CustomIP (
input [1:0] address,
input chipselect,
input clk,
input read,
input reset_n,
input write,
input [31:0] writedata,
output [9:0] led_out,
output reg [31:0] readdata
);
reg [9:0] DATA;
always @ ( posedge clk or negedge reset_n ) begin
if ( reset_n == 1'b0 ) begin
DATA <= 10'b0;
readdata <= 32'b0;
end else if ( chipselect && write && (address == 2'b0)) begin
DATA <= writedata[9:0];
readdata <= 32'b0;
end else if ( chipselect && read && (address == 2'b0) ) begin
readdata <= DATA;
DATA <= DATA;
end else begin
readdata <= 32'b0;
DATA <= DATA;
end
end
assign led_out = DATA;
endmodule
Save As : CustomIP.v
Add files to project:
  Project  Add/remove files in project
  Add custumIP.v to project

## Slide 4
In Main Quartus windows :
Tools  Platform Designer

## Slide 5: Adding Nios-II processor
  Find ‘nios’ in search box then choose Nios II Processor  click Add...
  then choose Nios-II/e  click Finish

## Slide 6: Adding Memory
  Find ‘memory’ in search box and choose On-Chip Memory (..) Intel FPGA IP  click Add...
  Then in field “Total memory size :” fill 40960 (bytes)  click Finish

## Slide 7: Adding JTAG
Find ‘jtag in search box and choose JTAG UART Intel FPGA IP  click Add...  click Finish

## Slide 8: Checkpoint-1
If all steps succeeded, it will looks like :

## Slide 9: Adding Custom IP
In IP catalog menu, click New Component  Add..

## Slide 10
on “Component Type” tab, fill :
Name : CustomIP
Display name : Custom IP
Version : ...whatever...
Group : ...whatever...
Description : ... whatever...
Created by : ... whatever...
Icon : ... whatever...

## Slide 11
On the “Files” tab in section “Synthesis Files”  “add File...” point to file CustomIP.v  click Open. After that, click “Analyze Synthesis File”

## Slide 12
It should be success, if syntax is not error at all  CLOSE

## Slide 13
Underside, in field “Verilog Simulation Files”, click “Copy from Synthesis Files”

## Slide 14
on “Signals & Interfaces” tab, click in “<<add interface>>” choose “Conduit”

## Slide 15
Choose signal “led_out[10] readdata”
drag-drop to under conduit 

## Slide 16
Change signal type “led_out[10]” from readdata to interface (whatever)
Change to 

## Slide 17
Click on “avalon_slave_0”
Ubah bagian “Associated Clock”  clock ; bagian “Associated Reset”  reset
Click Finish  Yes, Save

## Slide 18: Back to Platform Designer
In IP Catalog menu, our CustomIP already there
Click in CustomIP  add
Click finish

## Slide 19: All System in our SoC to be Integrated

## Slide 20
Click on Connection section,
So that connection is like this figure

## Slide 21: Assigning Base Address
Click on System  Assign Base Address

## Slide 22: Assign Processor Vectors
Click on “nios2_gen2_0”  Parameter window appear  click tab/menu ” Vectors“:
In section “Reset vector memory :” choose “onchip_memory2_0.s1”
In section “Exeption vector memory :” choose “onchip_memory2_0.s1”
close Parameter window

## Slide 23: Change Conduit name
Double-click in CustomIP_0, rightside of “Conduit” change to “LED_OUT”  enter

## Slide 24: Save SoC Design
Save this QSYS design as project_soc
(must be same as the quartus project name)

## Slide 25: Generate file HDL
Generate >> Generate HDL...  Generate  Close

## Slide 26: Generate Testbench
Generate >> Generate Testbench System...  Generate  Close

## Slide 27: Closing Platform Designer
Close Platform Designer with Clicking“Finish” di bottom-right corner of the window.
Will appear warning to include your *.qip file to quartus.project click OK

## Slide 28: Add files to Quartus Project
In Quartus main window, Project >> Add/Remove Files in Project...
Klik bagian “...” di sebelah kanan “File name”, dan arahkan ke folder Proyek_soc/synthesis dan pilih file Proyek_soc.qip  open  OK

## Slide 29: Analysis & Pin assignment
Do Analysis and Synthesis
Do Pin Planner :
  CLK pin
  10 led pin

## Slide 30: Software Part

## Slide 31: Nios-II Software IDE
Tools >> Nios II Software Build Tools for Eclipse

## Slide 32: Workspace Launcher.
  Point to folder where your quartus project is, then create new folder named Software, then choose that Software folder  klik Ok .
  (for example full folder name is D:\Altera\Design\Proyek_soc\Software)

## Slide 33
Then in Nios II – Eclipse windows, choose File >> New >> Nios II Application and BSP from Template

## Slide 34
  In Next windows, choose/fill :
    SOPC Information File Name : D:\Altera\Desain\Project_soc\Project_soc.sopcinfo
    Project Name : Nios-LED (must different with project name)
    Project Template : Hello World or Hello World Small
    click Finish

## Slide 35
Buka file hello_world.c
Save, then Compile file program : Project >> Build All
Change to 
#include "sys/alt_stdio.h"
#include "io.h"
#include "system.h"
int main()
{
printf ("Hello from Nios II!\n");
/* Event loop never exits. */
while (1){
IOWR(LEDS_0_BASE, 0, 0x155);
usleep(10000000);
IOWR(LEDS_0_BASE, 0, 0x2AA);
}
return 0;
}

## Slide 36: ELF file
If success, created :
*_onchip_memory*.hex
In mem_init folder

## Slide 37: Return to Platform designer
Choose komponen onchip_memory*, double-click
Check the “Enable non-default initialization file”
On user created file : point to C:/altera/project_soc/software/mem_init/*onchip_memory*.hex

## Slide 38: Compiling ALL
Re-generate the HDL File
Generate >> Generate HDL...  Generate  Close
Re-generate testbench
Generate >> Generate Testbench System...  Generate  Close
In quartus main windows, Processing  Start Compilation

## Slide 39: Program the board
Program the board like previous project
See what happen to the board